## Slide 1: Ising Machine
Dresden, August 20, 2024
Presenter: Yanxia Lu
Student ID: 5136301
Numerical Modelling
The Chair of High Frequency and Photonics Engineering

## Slide 2: Outline
Theoretical Fundamentals
Coherent Ising Machine
Learning Path along One Integrated CIM

## Slide 3: Theoretical Fundamentals
Ising Model (physics)
      Key components in Ising Model:
              Bistable spin states
              Interaction among spins
Pitchfork Bifurcation (mathmatics)
Spin up Spin down
Reisinger, Daniel, et al., PloS one 17.11 (2022): e0277347.
Marathe, A. and Govindarajan, R., 2014. Applied Mechanics Reviews, 66(2), p.024802.

## Slide 4: Coherent Ising Machine
Fiber Based Time-multiplexed CIM
Idler
Signal
Pump
FS, fiber stretcher;
LO, local oscillator;
BPF, band pass filter;
PSA, phase-sensitive amplifier.
BHD, balanced homodyne detector;
ADC, analog-to-digital converter;
DAC, digital-to-analog converter;
PMF, polarization-maintaining fiber.
T. Honjo, T. Sonobe, K. Inaba, et al., Sci. advances 7, eabh0952 (2021).
Notes: Time multiplexing mechanism in which the roundtrip length of the fiber feedback loop is precisely matched with an integer multiple of the pulsed pump’s repetition rate. Inside the feedback loop, a phase-sensitive amplifier made out of, e.g., periodically poled Lithium Niobate (PPLN), is used to create the DOPO which provides the required phase-bistability.

## Slide 5: Coherent Ising Machine
Chip-based Spatial-multiplexed
Idler
Signal
Pump 2
Pump 1
microheater
Aspheric lens
Free Space Michelson Interferometer
(Fiber Polarization
Controller)
(Bandpass Filter)
Erbium-doped Fiber Amplifier
Multimode Interference
Splitter
(Optical Spectrum Analyzer)
Y. Okawachi, M. Yu, J. K. Jang, et al., Nat. communications 11, 4119 (2020).

## Slide 6: Integrated CIM Based on Self-Phase Modulation in Microring Resonators
Integrated All-optical Ising Nodes without DOPO
    have pump input field of the same wavelength as the signal field.
    can be adapted to a variety of nonlinearities that can cause self-phase modulation, such as the thermo-optic, free-carrier dispersion and Kerr nonlinearity.
    cost less compared to fiber-based CIM using DOPO.
    A layer of neural nodes with nonlinear transfer function.
    (focus of the learning phase)
A multipath interferometer based on an MZI lattice that applies analog weights to the node outputs
Feedback paths connecting the outputs of the interferometer to the inputs of the nodes
N. Tezak et al., "Integrated Coherent Ising Machines Based on Self-Phase Modulation in Microring Resonators," in IEEE Journal of Selected Topics in Quantum Electronics, vol. 26, no. 1, pp. 1-15, Jan.-Feb. 2020, Art no. 5900115, doi: 10.1109/JSTQE.2019.2929184.

## Slide 7: Kerr Nonlinear Integrated Photonics
Modelling of Bistability of a Single Kerr-Nonlinear Resonator
Linewidth of the resonator:
Resonance angular frequency ω0, loaded quality factor: Q
The detuning of ω0 from the drive field: Δ = ω0 − ω
The dispersive non-linear coefficient: χ
The coherent normalized drive amplitude: u,
Input flux z is normalized # Photons in the resonator
Accoring to the paper:

## Slide 8: Bistability of a Single Kerr-Nonlinear Resonator
The pumping threshold to have multi-stability in a single nonlinear resonator:
      Based on the parameters given in
      paper, its working regime is 1.3 * Δth
Validate the relationship by recreating Fig. 2 of paper “Integrated Coherent Ising Machines Based on Self-Phase Modulation in Microring Resonators”.
N. Tezak et al., in IEEE Journal of Selected Topics in Quantum Electronics, vol. 26, no. 1, pp. 1-15, Jan.-Feb. 2020, Art no. 5900115, doi: 10.1109/JSTQE.2019.2929184.

## Slide 9: Tunable Amplifier with Feedback (TAFB)
Open-loop Amplifier Circuit
Closed-loop Tunable Amplifier
Thomas Van Vaerenbergh, et al., Proc. SPIE 10537, Silicon Photonics XIII, 105370D (14 March 2018); https://doi.org/10.1117/12.2288586
Tezak, N., Mabuchi, H. A coherent perceptron for all-optical learning. EPJ Quantum Technol. 2, 10 (2015). https://doi.org/10.1140/epjqt/s40507-015-0023-3
N. Tezak et al., IEEE Journal of Selected Topics in Quantum Electronics, vol. 26, no. 1, pp. 1-15, Jan.-Feb. 2020, Art no. 5900115, doi: 10.1109/JSTQE.2019.2929184.
better
footprint
spin interaction
through
Feedback coupling

## Slide 10: Spin Encoding
Input-output Relationship:
Define supermode:
And orthorgonal mode:
Spin encoding with s mode:
N. Tezak et al., IEEE Journal of Selected Topics in Quantum Electronics, vol. 26, no. 1, pp. 1-15, Jan.-Feb. 2020, Art no. 5900115, doi: 10.1109/JSTQE.2019.2929184.
DC
pump
u=u‘(p)
u‘
v(p)
Linearization of
nonlinear transferfunction
~ p
(+/- ~ 0/π)

## Slide 11: Steady State Photon Numbers
s mode bifurcation
mode instable
{,}, {}
{, }, {}
N. Tezak et al., IEEE Journal of Selected Topics in Quantum Electronics, vol. 26, no. 1, pp. 1-15, Jan.-Feb. 2020, Art no. 5900115, doi: 10.1109/JSTQE.2019.2929184.

## Slide 12
Near the pumping threshold, ξ can be expressed as approximate equations of motion
, whose Taylor expansion satisfies pitchfork bifurcation standard form:
Strogatz, S.H. (2015). Nonlinear Dynamics and Chaos: With Applications to Physics, Biology, Chemistry, and Engineering (2nd ed.). CRC Press.
https://doi.org/10.1201/9780429492563
That means there are two real solution to each pump power in this working regime. To understand this I have recreated the Fig. 4 of the original paper.
Tezak, N., Mabuchi, H. A coherent perceptron for all-optical learning. EPJ Quantum Technol. 2, 10 (2015). https://doi.org/10.1140/epjqt/s40507-015-0023-3
Phase sensitive amplifier gain grr (green, solid) , gir (red, dashed). gri (black ×’s) and gii (black dots).
There are two stable branches if 5th order term exists.
Notes: “There exists a certain input power range over which the out of phase quadratures of each oscillator are suppressed and the signs of the in-phase spin quadratures ξj can be use to encode the spins σj”

## Slide 13: Summary
The most important component for Ising machine is:
              Bistable spin states
              Interaction among spins
Nonlinear microring resonator (MRR) can work like a phase sensitive amplifier (PSA).
The supermode of individule MMR near pumping threshold can be encoded as spin states.
Possible improvement:
      Piezo-electrical tuning of a MRR  stronger nonlinearity
      Material with lower loss  scalability
      …